## Slide 1: MODFLOW Conceptual Models
CE EN 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 3: Steps
Build conceptual model object
Build coverages
Define grid frame
Build grid
Initialize MODFLOW
Activate cells in coverage
Map  MODFLOW

## Slide 4: 1. Build Conceptual Model Object
Used to organize conceptual model data
Defines flow package, transport option, species, etc.

## Slide 5: 2. Build MODFLOW Coverages
Any combination of coverages can be used
Select desired properties

## Slide 6: Conductances
Many of the objects in the Source/Sink category must be assigned a conductance value.
For arcs
  the conductance should be assigned on a conductance per length basis.
For polygons
  the conductance should be assigned on a conductance per area basis.
GMS computes length or area and computes and assigns the appropriate value.

## Slide 7: Arc Conductance

## Slide 8: Polygon Conductance

## Slide 9: Well Screens
Elevations entered for well screen as part of well properties
Layers and partitioned Q automatically assigned

## Slide 10: Auto Assign Elevations
Elevations entered at nodes as part of properties
Layers automatically assigned

## Slide 11: 3. Grid Frame
Defines location of grid relative to conceptual model
Can be used to rotate the grid
  Use Grid Frame tool to edit

## Slide 12: 4. Build Grid
Select “Map  3D Grid” command from Feature Object menu
Creates grid that fills grid frame

## Slide 13: 5. Initialize MODFLOW
Select “New Simulation” command in MODFLOW Menu in 3D Grid Module
Initializes MODFLOW data structures
Defines steady state vs. transient
Defines stress periods (if applicable)

## Slide 14: 6. Activate Cells in Coverage
Select the “Activate Cells in Coverage(s)” command in Feature Objects menu
Inactivates all cells outside of conceptual model boundary

## Slide 15: 7. Map  MODFLOW
Select conceptual model in Project Explorer
Select the “Map  MODFLOW” command in Feature Objects menu
Discretizes model input